## Slide 1
GRANICA × IIT GUWAHATI PRESENTER: DAKSH AGARWAL
The Invisible Wall: Why Campus Wi-Fi Fails Inside Student Rooms
THE USER
Campus IT & Hostel LAN Committee
7,000+
STUDENT RESIDENTS
Responsible for maintaining continuous network operations and wireless coverage across sprawling student hostels and common campus spaces.
THE PROBLEM
Hallway Optics vs. Room Reality
Central IT monitors routers positioned in central hallways, showing healthy traffic and optimal signal levels.
Physical Barriers: Concrete walls and solid doors absorb radio waves heavily.
User Impact: Frozen video calls and UPI payment timeouts (e.g., in the Canteen).
Visibility Gap: Central IT lacks telemetry on actual RF absorption inside rooms.
THE CORE QUESTION
Diagnosing the Physical Layer
1. Signal Attenuation
How much Wi-Fi signal do structural barriers actually absorb?
2. Automated Remediation
How can ordinary client devices help IT automatically locate & fix physical deadzones?

## Slide 2
METHODOLOGY & SYSTEM ARCHITECTURE
End-to-end telemetry pipeline, passive client probing, and physics-informed wave regression.
SYSTEM PIPELINE
The Workflow
1. Signal Propagation
Radio waves strike physical barriers.
2. Passive Probing
Client smartphones passively probe beacon frames.
3. Telemetry Ingestion
Scans saved directly to Apache Parquet dataset.
4. Physics Regression
Model isolates exact barrier absorption.
5. Actionable Alerting
Generates automated IT support tickets.
EDGE PROBING
Data Collection
Used Open-Source WiFi Analyzer on commodity smartphones to capture raw 802.11 beacons, link rates and ping RTT.
120 On-Site Scans
Surveyed across 8 distinct campus environments with 240 ITU-R calibrated extensions.
HOSTEL ROOM METRIC
Door Open: 144 Mbps
Door Closed: 58 Mbps
MODEL FITTING
RF-Pulse Solution
Ridge regression fitted on log-distance wave propagation.
R² = 0.935
MODEL ACCURACY
Learned Physics Constants:
• Waveguiding (Hallway): n = 1.84
• Door Attenuation: +12.8 dBm
• Wall Attenuation: +4.4 dBm
Integrated with multi-surface tooling for continuous campus-wide calibration.
GRANICA × IIT GUWAHATI

## Slide 3
RESULTS & OPERATIONAL ACTION
+12.8 dBm
DOOR LOSS FINDING
Closing a hostel door cuts signal power by >90%, causing a 59.7% speed drop (144 to 58 Mbps).
94m
CANTEEN DEADZONE
Severe path-loss (-87.3 dBm) explains daily UPI payment failures across campus.
0.935
R² MODEL ACCURACY
Log-distance physics model explains 93.5% of campus-wide signal variance.
ACTIONABLE IT IMPACT
Generates automated remediation directives:
Relocating corridor Access Points by 1.8m for optimal coverage.
Installing a dedicated Canteen Access Point to resolve path-loss.
Overriding roaming thresholds to -72 dBm.
PROJECT ARTIFACTS & LINKS
Live System & Source Code Access
SYSTEM DASHBOARD
Local System Dashboard (via python –m web.server)
REPOSITORY
https://github.com/hskad/rf-pulse
GRANICA × IIT GUWAHATI
SCALING UP
Put into student apps to detect deadzones in the background.
Let campus Wi-Fi routers adjust its own power and channels automatically